Back-plane Setup
# Connectors
Four PCIe connectors creating a possible 98 Pins Per card.
## Power Pins
- A1 – 24V
- A2 – 12V
- A3 – 5V
- A4 – 3.3V
- A32 – GND
## Setup Pins
Setup pins are used to help master card to self arrange to detect what card and what pins are being used by each card in each slot. A simple RxTx CS setup using possibly I2C can send from the slave when Rx is high what pins are used.
The RxTx CS pins are:
- A5 – Rx
- A6 – Tx
- A7:A9 – CS
## Analog Pin Range
A10 – A31
## Digital Out Pin Range
B1 – B16
## Digital In Pin Range
B15 - B32
## PWM Out Adapter Pins
C1 – C10
## PWM Response Signals
C11 – C20
## Ligh and Safety Pins
C21 - C32